15.01.2010

HAREKET Proje Taşımacılığı

Specification for chassis

| Variant Description | TGX 41.680 8X4/4 BBS |
| --- | --- |
| Basic vehicle number: | L94XKR65-00000 |
| Type of vehicle: | Semitrailer tractor, Conventional |
| Cab: | XXL Cab with high roof |
| Wheelbase: | 2600 mm |
| Overhang: | 0725 mm |
| Steering: | L |
| Front-axle load: | 8000 Kg |
| Rear axle load: | 33500 Kg |
| Perm. gross weight | 41000 Kg |

Tyres

| Front axle | 2 * 81#R0080592 MI 385/65R22,5 XF2 TL 160 K Strg-Lh |  |
| --- | --- | --- |
| Second steering axle | 2 * 81#R0080592 MI 385/65R22,5 XF2 TL 160 K Strg-Lh |  |
| Rear axle | 4 * 81#R0080530 MI 315/80R22,5 XDY3 TL 156/150 K Drive-S + G |  |
| 2nd rear axle | 4 * 81#R0080530 MI 315/80R22,5 XDY3 TL 156/150 K Drive-S + G |  |
| Spare wheel | 1 * 81#R0080592 MI 385/65R22,5 XF2 TL 160 K Strg-Lh |  |

Colours

| chassis | 9011 graphite black RAL 9011 matt | W |  |
| --- | --- | --- | --- |
| wheels | 9006 White aluminium acrylic RAL 9006 | N |  |
| cab | 9010 Pure white RAL 9010 | N |  |

Customer specification: equipment for vehicle TGX 41.680 8X4/4 BBS / L94XKR65-00000

Engine Cooling System Clutch

| 018YLS | MAN 8-cylinder 4-valve V8 engine D2868LF06, displacement 16160 ccm, with Common Rail injection, turbocharging and intercooling, EDC engine regulation, rating 680 hp / 500 kW at 1900 rpm, torque 2700 Nm, at 1100 - 1700 rpm, low-pollutant exhaust gases to EURO5 and EEV standard. SCR catalyst and AD-Blue injection. With on-board diagnosis system (OBD2) and NOX control. |  |
| --- | --- | --- |
| 124ARS | additional fuel filter heated with water trap, make SEPAR |  |
| 203ESM | Steuermodul f. ext. Datenaustausch (KSM)m. Flotten-Management-Systemschnittstelle(FMS)Aufbaufunktionalität |  |
| 208ALS | Controlled MAN Exhaust Valve Brake EVBec. Can also be triggered by Brakematik. The brake power of this EVB is optimally controlled by butterfly valve actuating cylinders. Comprises V-constant control (Constant braking). If cruise control is set this permits constant speed on downhills by triggering the continuous brakes as required. |  |
| 210AAS | flame starting system |  |
| 211FRS | Ceram clutch if WSK fitted |  |
| 542BAM | low-noise certification for Austria and L plate |  |
| 542BCM | COP document |  |
| 542BKM | exhaust gas certificate Euronorm |  |

Intake / Exhaust System

| 206TAM | Tailpipe elbow for raised or vertical exhaust |  |
| --- | --- | --- |

Gearbox

| 022TOS | Getriebe ZF 12 AS 2740 OD, 12 Vorwärts- 2 Rückwärtsgänge, Übersetzungsbereich 12,33 - 0,78, geeignet für Zuggesamtgewichte bis 250 t (unter Beachtung der Schwertransport Information!). Automatisiertes Klauengetriebe. Mit MAN TipMatic: Schaltung und Kupplu |  |
| --- | --- | --- |

Power Take-Offs

| 212AAM | Gearshift lock. When the power take-off is engaged no gear can be engaged in the gearbox. |  |
| --- | --- | --- |

Front Axle / Front Springs / Front Axle Load

| 026EFM | Low-friction parabolic springs, 9.5 t, with, shock absorbers. |  |
| --- | --- | --- |
| 534FRW | Permissible FA load 9000 kg. Note tyre load rating. |  |

Rear Axle / Rear Springs / Rear Axle Load

| 028FPM | rear springs parabolic 16 t |  |
| --- | --- | --- |
| 034MSM | MAN hub reduction rear tandem axle AP HPD-1682/HP-1652. Gross train weights: for i <= 4.0: 70 t (for heavy-duty transport for up to 10 % 160 t, otherwise up to 120 t). For i > 4.0: 82 t (for heavy-duty transport up to 250 t). See heavy-duty transport fitting requirement information. For actual axle loads see load variants. |  |
| 535TNW | permissible leading/rear axle load 8000/2 X 13000 kg |  |

Transmission ratios

| 035FAW | planetary axle ratio i = 4.83 |  |
| --- | --- | --- |

Rims

| 038GHM | Disc wheels, 10-hole, 11.75 x 22.5 on 1st front axle TL. Extra weight 2x 8 kg compared to 9.00- 22.5 wheels. |  |
| --- | --- | --- |
| 038SHM | Disc wheels, 10-hole, 11.75 x 22.5 on leading axle TL. Extra weight 23 kg per complete 385/65R 22.5 wheel compared to 315/70 R 22.5 |  |
| 038THM | Aluminium disc wheels, 10-hole, 11.75 x 22.5 as spare wheel TL. Extra weight 23 kg per complete 385/65 R 22.5 wheel compared to 315/70 R 22.5. |  |

Fuel Tanks

| 123CCM | strainer for fuel tank |  |
| --- | --- | --- |

Frame

| 233EMM | Three-piece steel bumper, new version for optimum passage of cooling air. This makes gross train weights with polyurethane and steel pumps identical. If the vehicle has a front underride guard no radiator guiard is possible. The robust three-piece steel bumper is the optimal equipment for all vehicles used off-road and on construction sites. |  |
| --- | --- | --- |
| 236FAM | rear cross member for heavy transp. and standard trailer coupling normal and heavy transp.coupling low |  |
| 294AAM | support plate for gooseneck (low-loader) |  |

Trailer/Fifth-wheel Coupling

| 491CCM | JOST JSK 38 G - 1 3/5" fifth-wheel coupling, height 290 mm, with cardan suspension. Also suitable for off-road use. Max. fifth-wheel load 36000 kg, D value 260 kN, weight approx. 265 kg, connecting hole pattern to DIN 74081 and ISO 3842. |  |
| --- | --- | --- |

Brake System

| 034ECS | brake shoe width for rear axle 220 mm |  |
| --- | --- | --- |
| 045AEM | Bus-stop brake. If gear lever is in neutral and pto engaged the brake cylinders can be pressurised. |  |
| 261ACM | brake connection front 2-line |  |
| 262AHM | additional 2-line brake connection at end of frame |  |
| 262EFM | Aluminium air tanks Weight saving for 4x2: 10 kg, for 6x2 and 6x4: 15 kg. |  |
| 265AFM | parking brake with pneumatic application of front wheel brakes |  |

Cab exterior

| 050NHS | XXL cab, 2440 mm wide, 2280 mm long. Maximum interior space for most exacting comfort requirements even with 2 drivers. Very large number of storage facilities. High position of the cab gives excellent view and low engine hood permits easy changing to the co-drivers seat. High seating position for good view. |  |
| --- | --- | --- |
| 150AZM | In lhd vehicles the cab tilt mechanism in on the right side behind the bumper. The tilt mechanism is simple and functional in design. The rockers permit a cab tilt angle of over 65° (F2000: approx. 50°) and thus better access to engine and components for maintenance and repair work. Electrically operated. |  |
| 388AKM | The sun visors are fastened with 4 high-strength plastic brackets. At the side they are also supported by the mounts for the marker lights. The visor brackets are prepared for additional attachments. |  |

Cab interior

| 058NKM | ISRINGHAUSEN high-comfort driver's seat with climate control. Unique sitting experience for the driver and maximum comfort whatever the weather. A barely perceptible temperature-controlled micro-airflow cools and dries the contact faces on cushion and backrest. If necessary the integrated heater provides the necessary warmth. |  |
| --- | --- | --- |
| 059NHM | High-comfort co-driver's seat from a new generation in design, comfort and operation. Fittings: air suspension, integrated belt system, storage pocket and ventilation slits on seat back. |  |
| 153EYM | EBERSPÄCHER AIRTRONIC D4S is a diesel/air heater with a maximum heat output of 3.5 kW. Temperature can be set at a clock with thermostat function. Heat output is controlled in 4 stages from 1000 to 3500 W. The heater is under the co-driver's footwell. The |  |
| 276ACW | armrests for driver's seat |  |
| 278EAM | The air connection in the cab takes air from the existing circuit for seat, air horn etc. For this a hose connection with wing nut cap is fitted under the bottom bunk near the stowage box behind the bulkhead. |  |
| 390ATM | The storage box is stowed under the bunk and can be pulled out. It has two compartments inside: up to three 2 l bottles will fit in the first compartment, while the compartment behind can be used for other utensils.. |  |

Instruments

| 042FPM | EC tachograph electronic - 2 drivers with add. recorder for tankers (no EU-approval since 2006) |  |
| --- | --- | --- |
| 325EZW | language 1 'Turkish' for display in instrument panel |  |
| 339ANM | crankshaft revolutions counter |  |
| 339FKM | Trailer data display in instrument panel. Tyre pressure management TPM for correspondingly equipped trailers. The pressure signals from the trailer are shown in the display via the vehicle's CAN bus. In this way most tyre damage can be prevented. |  |
| 339FLM | Trailer data display in instrument panel. Brake pad check system for correspondingly equipped trailers. The pad thicknesses in the trailer are shown in the display via the vehicle's CAN bus. In this way servicing of brakes can be optimised. |  |
| 339FMM | Trailer data display in instrument panel. Axle load check system for correspondingly equipped trailers. The axle load signals from the trailer are shown in the display via the vehicle's CAN bus. |  |

Lights

| 310CLM | Foglamps and additional high-beam headlights are grouped in single housings. One free-form reflector is used for both units, and one standard H4 lamp fulfils both functions. The high-beam filament is used for the additional headlight and the low-beam fila |  |
| --- | --- | --- |
| 310FRM | 2 spotlights on rack behind cab |  |
| 352EPM | 2 halogen revolving beacons yellow on cab roof left and right |  |
| 353CAM | A light under the middle step on the co-driver's side, operated from switch in dashboard, lights up the area in the ramp mirror on the co-driver's side and thus assists in manoeuvring in the dark. The driver can thus recognise the road condition and obstacles on the co-driver's side better. |  |

Electrical System

| 324CAM | 2 air horns on cab roof |  |
| --- | --- | --- |
| 326CKM | Trailer socket for ABS at frame end |  |
| 326CWM | Trailer socket, 24 V, 7 + 7 pole, for reversing light and rear foglamp at frame end. 1 socket for normal trailer lighting. 1 socket for rear foglamp and reversing light |  |
| 326MTM | socket 24V 7+7-pole at front |  |
| 327AFM | battery main switch, mechanical |  |

For Special Vehicles

| 124FRM | hydraulic fluid reservoir aluminium 300l on rack behind cab |  |
| --- | --- | --- |
| 240EUM | front plate for heavy transport coupling |  |
| 280ACW | wiring for tank truck to ADR |  |

Other

| 277APW | BEKA-MAX fully automatic central lubrication system for fifth-wheel coupling. |  |
| --- | --- | --- |
| 405CPM | 20 m tyre inflator hose with pressure gauge |  |
| 405FDM | 2 warning flashers loose |  |
| 407AAM | jack 25 t |  |
| 490TCM | 3-stage hydraulic system for heavy- duty transport with connections on rack behind cab, engine-dependent |  |
| 490TEM | additional hydraulic connections at frame end for heavy-duty transport |  |
| 490TFM | additional hydraulic connections at front cross member for heavy-duty transport |  |

Load variants and miscellaneous

| 007NXW | gross combination weight 250 t |  |
| --- | --- | --- |
| 524JPW | load variant 44000 kg |  |

Auxiliary equipment ex works

| ZW006M | entry in reg.document: RA load up to 16.0t only if max.speed 40 km/h; up |  |
| --- | --- | --- |

İlktuğ Çağatay Kepek

MAN Kamyon ve Otobüs Tic. A.Ş.

Vehicle data Power train  - TGX 41.680 8X4 4 BBS   L94XKR65-HAREKET

| Truck train: | Semitrailer train |
| --- | --- |
| GTW [kg] | 44000 |
| Design speed [km/h]/engine speed at design speed [rpm] | 89/1670 |
| Residual climbing ability in the highest gear at design speed [%] | 3,2 |

Engine

| Sales code | Designation | Performance | Start of green speed range | End of green speed range | Max. speed |
| --- | --- | --- | --- | --- | --- |
| 018YL | engine D2868LF06 - 680 hp / 500 kw EURO5 SCR 2700 Nm V8 C-R OBD2 | 680 | 1220 | 1310 | 1900 |

Gearbox

| Sales code | Designation | Transmission intervals | max. GCW | Forward gears | Reverse gears |
| --- | --- | --- | --- | --- | --- |
| 022TO | gearbox ZF 12 AS 2740 OD MAN TipMatic with WSK440 and retarder | 12,33-0,78 | 250000 | 12 | 2 |
| Forward gears | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| Transmission | 12,33 | 9,59 | 7,44 | 5,78 | 4,57 | 3,55 | 2,70 | 2,10 | 1,63 | 1,27 | 1,00 | 0,78 |

Rear axle

| Sales code | Designation | Design | Load capacity | Transmission | max. GCW |
| --- | --- | --- | --- | --- | --- |
| 034MS | hub-reduction rear axle HPD-1682/ HP-1652 | AP | 32000 | 4.83 | 80000 |

Tyres (rear axle)

| Tread pattern | Sales group | Diameter | Circumference | Single load | Double load | SI |
| --- | --- | --- | --- | --- | --- | --- |
| MI 315/80R22,5 XDY3 TL 156/150 K Drive-S + G | 81#R0080530 | 1098 | 3350 | 4000 | 3350 | K |

Traction

| Skid point [%] | 40 | Condition of the ground | Road |
| --- | --- | --- | --- |
| Moving-off behaviour in the lowest gear [%] | 22 | at eng. speed [rpm] | 1100 |

Speed (On-road gears): at max. eng. speed

Climbing ability (On-road gears): Road

Chassis - TGX 41.680 8X4 4 BBS   L94XKR65-HAREKET

| Cab: | XXL Cab with high roof |
| --- | --- |
| Wheelbase/overhang | 2600/725 |

Semitrailer:

| Width: | 2440 |
| --- | --- |
| Height: | 2682 |
| Max. overall height: | 4000 |
| Distance to cab: | 240 |
| Weight of fifth-wheel coupling: | 135 |
| Semitrailer weight: | 0 |
| Max. payload (calculated): | 27125 |

Chassis:

| Load capacity: | 27320 |
| --- | --- |
| Perm. weight: | 41000 Kg (8,0/7,5/13,0/13,0) |

Tyres:

| Diameter: | 1098 |
| --- | --- |
| tFA: 385/65R22.5 | 30 Kg Change tyres |
| tRA: 315/80R22.5 | 30 Kg Change tyres |

Pickup plate:

| Fifth-wheel height unladen/laden | 1141/1071 |
| --- | --- |
| Fifth-wheel coupling height: | 185 |
| Fifth-wheel lead: | 1201 |

Table of axle loads:

| Weight distribution | Centre of gravity to tFA | at front (kg) | % | at rear (kg) | % | total (kg) | % |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Chassis incl. change of tyres |  | 7450 | 18,1 | 6290 | 15,3 | 13740 | 33,5 |
| Fifth-wheel coupling |  | 38 |  | 97 |  | 135 |  |
| Load capacity / payload | 4249 | 128 | 0,3 | 27192 | 66,3 | 27320 | 66,6 |
| Body empty 3402 | 4249 | 0 | 0 | 0 | 0 | 0 | 0 |
|  |  | ====== |  | ====== |  | ====== |  |
| Overall load |  | 7616 | 18,5 | 33579 | 81,9 | 41195 | 100,4 |
| Max.axle loads |  | 8000 |  | 33500 |  | 41000 |  |
| Load reserve (+)/overload (-) |  | 384 |  | -79 |  | -195 |  |
|  |  | ---------- |  | ---------- |  | ---------- |  |
| Chassis dead weight (standard) |  |  |  |  |  | 13680 |  |
| Change tyres |  |  |  |  |  | 60 |  |
|  |  |  |  |  |  | ---------- |  |
| Corr. dead weight |  |  |  |  |  | 13740 |  |

Payload diagram - TGX 41.680 8X4 4 BBS   L94XKR65-HAREKET

Heights sheet - TGX 41.680 8X4 4 BBS   L94XKR65-HAREKET

Length diagram - TGX 41.680 8X4 4 BBS   L94XKR65-HAREKET